## Slide 1
DECK 1
Device Troubleshooting
Teach students to preserve known-good checkpoints and isolate the first failed dependency.
Free PowerPoint Deck • Evidence-first classroom design
AP Networking Exam Prep

## Slide 2
AP Networking Exam Prep
Deck 1
The device troubleshooting loop
1
Scope the complaint
2
Compare a working peer
3
Check access/link
4
Read IP state
5
Test gateway
6
Separate DNS/service
Students should name the first unresolved dependency before choosing a fix.
Independent classroom resource • Not affiliated with College Board
2

## Slide 3
AP Networking Exam Prep
Deck 1
What the working peer controls
Working peer proves
• Shared access network can support that peer
• Gateway and upstream path work for the peer
• A same-destination comparison is possible
Working peer does not prove
• Affected device has correct settings
• Every path, protocol or service works
• The failure is always user error
Independent classroom resource • Not affiliated with College Board
3

## Slide 4
AP Networking Exam Prep
Deck 1
Artifact slide: two endpoints
Field
Working peer
Affected laptop
Teaching question
IPv4
10.20.30.18
10.20.30.44
Same subnet?
Mask
255.255.255.0
255.255.255.0
Same local boundary?
Gateway
10.20.30.1
10.20.99.1
Which remote dependency fails?
DNS
10.20.10.53
10.20.10.53
Is DNS first?
Local peer ping
Pass
Pass
What is known good?
Independent classroom resource • Not affiliated with College Board
4

## Slide 5
AP Networking Exam Prep
Deck 1
Misconceptions to engineer
Wrong layer
Changing DNS does not fix a wrong gateway when name resolution has not yet been tested.
Overclaim
Local peer success does not prove remote routing, but it does prove the client can communicate locally.
Shotgun fix
Changing gateway, DNS and cable together restores service but destroys causal evidence.
Weak verification
A gateway ping after fixing the gateway is not enough if the original task was a remote application.
Independent classroom resource • Not affiliated with College Board
5

## Slide 6
AP Networking Exam Prep
Deck 1
Board prompt sequence
Predict
With this wrong gateway, what should still work and what should fail?
Claim
What is the smallest conclusion supported by the artifact?
Falsify
What result would weaken the gateway hypothesis?
Verify
Which original test must pass after the correction?
Independent classroom resource • Not affiliated with College Board
6

## Slide 7
AP Networking Exam Prep
Deck 1
Mini diagram: local vs remote
Local delivery
Client
Peer
Remote delivery
Client
Gateway
Server
If the gateway field is wrong, local delivery can pass while remote delivery fails.
Independent classroom resource • Not affiliated with College Board
7

## Slide 8
AP Networking Exam Prep
Deck 1
Exit ticket
Claim + evidence + boundary + verification
Students must explain which dependency failed, cite the exact field/output, state what the evidence does not prove, and name the test that verifies the original requirement.
Independent classroom resource • Not affiliated with College Board
8