## Slide 1
DECK 4
Routing & CLI Evidence
Use destination-driven route selection, command outputs and bounded inferences.
Free PowerPoint Deck • Evidence-first classroom design
AP Networking Exam Prep

## Slide 2
AP Networking Exam Prep
Deck 4
Route selection sequence
1
Resolve destination
2
Find matching routes
3
Select longest prefix
4
Check next hop
5
Test forwarding
6
Check return path
Metrics are considered only after the destination has matching comparable routes.
Independent classroom resource • Not affiliated with College Board
2

## Slide 3
AP Networking Exam Prep
Deck 4
Route-table artifact
Prefix
Next hop
Metric
Matches 10.40.8.25?
10.40.8.0/24
10.20.1.1
20
Yes — most specific
10.40.0.0/16
10.20.2.1
5
Yes — less specific
10.0.0.0/8
VPN0
1
Yes — less specific
0.0.0.0/0
ISP
10
Yes — least specific
Independent classroom resource • Not affiliated with College Board
3

## Slide 4
AP Networking Exam Prep
Deck 4
Command by question
What is my config?
Use IP configuration output before guessing DHCP/DNS/gateway problems.
Which path is selected?
Use route output for the exact destination.
Can the name resolve?
Use DNS query output, not only browser errors.
Is service reachable?
Use an exact TCP/service test, not only ping.
Where is L2 learned?
Use ARP/neighbor/MAC table artifacts.
What changed over time?
Use logs and counter deltas, not snapshots only.
Independent classroom resource • Not affiliated with College Board
4

## Slide 5
AP Networking Exam Prep
Deck 4
Ping and traceroute boundaries
Ping can support
• A tested ICMP exchange succeeded or failed
• A basic reachability checkpoint for that protocol
• A comparison across sources/destinations
Ping cannot prove
• TCP/443 is permitted
• DNS is correct
• The application is healthy
• All routers forward all traffic
Independent classroom resource • Not affiliated with College Board
5

## Slide 6
AP Networking Exam Prep
Deck 4
Traceroute caution
An asterisk is not a root cause.
A missing diagnostic response may mean filtering, deprioritization or path behavior. Pair traceroute evidence with route, next-hop and destination-specific controls.
Independent classroom resource • Not affiliated with College Board
6

## Slide 7
AP Networking Exam Prep
Deck 4
Return-path case
Forward evidence
• DNS returns correct server IP
• Client route selects intended path
• Server log records request timestamp
Next branch
• Response route from server
• Server default gateway
• Stateful firewall return behavior
• Asymmetric path compatibility
Independent classroom resource • Not affiliated with College Board
7

## Slide 8
AP Networking Exam Prep
Deck 4
CLI exit ticket
Claim
State the smallest supported conclusion.
Evidence
Cite exact output values.
Boundary
State what the output does not prove.
Next test
Choose an artifact that separates remaining causes.
Independent classroom resource • Not affiliated with College Board
8