## Slide 1
DECK 2
SOHO Troubleshooting
Break the all-in-one router into access, DHCP, DNS, NAT, WAN and service functions.
Free PowerPoint Deck • Evidence-first classroom design
AP Networking Exam Prep

## Slide 2
AP Networking Exam Prep
Deck 2
One box, many functions
Access point
Visibility, association and authentication can fail before IP configuration.
Switch
Wired clients may work even when radio functions fail.
DHCP server
New clients can fail while existing leases keep working.
DNS forwarder
Remote numeric IP can work while names fail.
NAT/firewall
Private-to-public flows need matching translation/policy.
WAN edge
Link, address, route and provider reachability are separate.
Independent classroom resource • Not affiliated with College Board
2

## Slide 3
AP Networking Exam Prep
Deck 2
Scope drives the branch
Scope
Likely first branch
Good control
One laptop fails
Endpoint config/security
Peer on same SSID
Wi-Fi only fails
Radio/auth/VLAN/DHCP
Wired client through same gateway
All clients, local works
WAN/NAT/DNS/provider
Gateway + local printer
Remote IP works, names fail
DNS forwarder/resolver
Direct query to intended resolver
One app fails
Destination/service/policy
Other app + same app from peer
Independent classroom resource • Not affiliated with College Board
3

## Slide 4
AP Networking Exam Prep
Deck 2
Wireless state machine
1
SSID visible
2
Associate
3
Authenticate
4
Get IP
5
Reach gateway
6
Reach remote
7
Resolve name
Students should not troubleshoot DHCP until they know the client passed the earlier wireless states.
Independent classroom resource • Not affiliated with College Board
4

## Slide 5
AP Networking Exam Prep
Deck 2
Case: wired works, Wi-Fi auth fails
Evidence
• Wired desktop opens sites
• Wireless clients see SSID
• Wireless clients cannot authenticate
• No IP lease yet
Supported next step
• Do not blame ISP first
• Inspect wireless security mode and credentials
• Check AP/auth logs
• Verify authorized succeeds and invalid fails
Independent classroom resource • Not affiliated with College Board
5

## Slide 6
AP Networking Exam Prep
Deck 2
WAN evidence ladder
Gateway reachable
LAN path works for tested traffic.
WAN link up
Provider handoff shows link, not Internet service.
WAN address present
Addressing exists, but route/upstream can still fail.
Provider next hop fails
Escalation boundary becomes stronger.
Independent classroom resource • Not affiliated with College Board
6

## Slide 7
AP Networking Exam Prep
Deck 2
DNS forwarder case
Test
Result
Inference
Client → gateway
Pass
LAN and local gateway path work
Client → remote numeric IP
Pass
Routed IP path works without DNS
Client → gateway DNS query
Timeout
Shared DNS forwarder path/service unresolved
Alternate resolver control
Works
Client can use DNS path elsewhere
Original name after repair
Pass
Requirement matched
Independent classroom resource • Not affiliated with College Board
7

## Slide 8
AP Networking Exam Prep
Deck 2
Reboot is not root cause
“It worked after reboot” is restoration evidence.
Capture WAN address, DNS state, DHCP leases, uptime, logs and repeatable tests before restarting when practical. A reboot can renew, clear or restart many functions.
Independent classroom resource • Not affiliated with College Board
8