## Slide 1
DECK 3
Switching, VLANs & Segmentation
Teach students to trace frames, VLAN placement, trunks and exact firewall policy.
Free PowerPoint Deck • Evidence-first classroom design
AP Networking Exam Prep

## Slide 2
AP Networking Exam Prep
Deck 3
Frame decision sequence
1
Receive frame
2
Identify VLAN
3
Learn source MAC
4
Look up destination
5
Forward / flood / filter
Switching vocabulary matters because each term names a forwarding decision.
Independent classroom resource • Not affiliated with College Board
2

## Slide 3
AP Networking Exam Prep
Deck 3
MAC table artifact
MAC
VLAN
Port
Student question
00:11:22:AA:10:01
20
Gi1/0/8
Expected user port?
00:11:22:AA:10:02
20
Gi1/0/24
Expected trunk?
00:11:22:AA:10:03
30
Gi1/0/8
Why is same port learning another VLAN?
Many MACs
20
Gi1/0/23 ↔ Gi1/0/24
Loop or topology event?
Independent classroom resource • Not affiliated with College Board
3

## Slide 4
AP Networking Exam Prep
Deck 3
Selective VLAN trunk failure
Observed
• VLAN 10 crosses trunk
• VLAN 20 crosses trunk
• VLAN 30 works locally on both switches
• VLAN 30 fails across trunk
Best next evidence
• VLAN 30 exists on both switches
• VLAN 30 allowed/active on trunk
• Tag/native expectations consistent
• Do not replace cable first
Independent classroom resource • Not affiliated with College Board
4

## Slide 5
AP Networking Exam Prep
Deck 3
Segmentation rule anatomy
Source
Which subnet, VLAN, role or zone initiated the flow?
Destination
Which host, subnet or application is targeted?
Service
Protocol and destination port must match the requirement.
Order
An earlier broad deny can shadow a later permit.
State
Return traffic may depend on stateful behavior.
Verification
Allowed flow succeeds; prohibited control remains denied.
Independent classroom resource • Not affiliated with College Board
5

## Slide 6
AP Networking Exam Prep
Deck 3
Rule-order artifact
Order
Source
Destination
Service
Action
5
StaffNet
ServerNet
Any
Deny
20
StaffNet
AppServer
TCP/443
Allow
Question
10.20.0.44
10.40.0.25
TCP/443
Which rule wins?
Independent classroom resource • Not affiliated with College Board
6

## Slide 7
AP Networking Exam Prep
Deck 3
Do not flatten segmentation
A symptom can disappear while the design becomes wrong.
Moving guests to trusted VLANs, permitting every VLAN on trunks, or adding any-to-any rules may restore a test but violate the segmentation requirement.
Independent classroom resource • Not affiliated with College Board
7

## Slide 8
AP Networking Exam Prep
Deck 3
Positive + negative tests
Positive
StaffNet reaches the approved HTTPS learning server.
Negative
GuestNet remains denied to the management subnet.
Mechanism
The intended rule matches the exact flow.
Guardrail
Other VLANs remain correctly isolated and carried.
Independent classroom resource • Not affiliated with College Board
8